This low cost chip (around $0.03) is in some solar/battery lamps. It may be useful to hobby projects, but I couldn't find find the english-language spec sheet, so I translated from https://detail.1688.com/offer/1031982265.html

0119A (solar lawn lamp) LED driver chip
 0119A is a dedicated single battery-powered solar lawn lamp drive control circuit, which has an integral charge control and the drive control circuit of two parts; a charging control section to complete the solar panel (hereinafter referred to as energy board) level detection, charge control and battery current anti-intrusion and other functions; the drive control section to complete the rechargeable battery (hereinafter referred to as cell) level detection, generates a pulse wave, the manual standby and maximum peak current limiting. The circuit requires only a peripheral inductive element, can form STEP-UP-type switching power supply system, and the charging efficiency and drive the highest efficiency values ​​in excess of 80%. The circuit has high efficiency, low power consumption, operating voltage as low as 0.80V, charging can be done automatically and drive functions and other characteristics, especially suitable for single-cell powered lighting solutions, often used for outdoor solar lawn lights, solar landscape lights, small solar street lamps.

Product Features
- Simple peripheral circuit components for a variety of LED driver, and you can select the photoresistor solar panels and light control.
- Low voltage applications: 0.80V ~ 2.4V;
- Over-discharge protection: voltage is lower than 0.9V, the system is closed and latched open until the next night.
- Output Current: 1.0V ~ 1.3V between the output constant current output, 0.9V or less current rapid decline;
- High efficiency: 80%
- TO-94 package

Advantage Supply:

- 1.2v (a battery) ANA618 efficiency up to 90% of the periphery of only one inductor solar lawn IC;
- 1.2v (a battery) ANA618 efficiency up to 90% of the periphery of only one inductor solar lawn IC;
- 1.2V (one cell) ANA608 efficiency up to 90% consistency, a high stability of solar lawn IC;
- 2.4v (two batteries in series) ANA609 two dedicated battery, up to 90% efficiency, consistency, a high stability of solar lawn IC;
- 1.2V (one cell) ANA650 maximum 100MA, steady and flashing two modes solar lawn IC / spike lights IC;
- 1.2V-2.4V (a battery or two batteries in series) 0116 Optional light control sensitive solar panel solar lawn IC;
- 1.2V-2.4V (a battery or two batteries in series) 0119 discharge protection, 1.0v or more constant, solar lawn IC;
- 3.6V (three cells in series) 0122 (a battery) 3.6V maximum 300MA, step-down constant current solar lights IC;
- 1.2V (a battery) 0120 (a battery) Solar candle lights IC;
- 1.2v (a battery) QX5252F (TO-94) Solar Lawn IC;
- 1.2V (one cell) QX5252E (DIP8) solar lawn IC;
- 1.8-3.0V (two batteries in series) QX5253 (DIP8) solar lawn IC.

TO-94 pinout (facing narrower side):

1. SBAT
2. BAT
3. GND
4. LX